## Slide 1
A Point of View : Solution construct
– Creating a Tailor Made solution for Client

## Slide 2
Temperature
Level
Pressure
Flow
Differential Pressure Switch
Vibration
Current
Voltage
Contamination
Position
Comm status
On/Off FeedClientck
Gap
Offset
Profile/Ovality
Tank Hydraulic Oil
Electrical Panel Room Temp.
Water-in Hydraulic oil cooling
Water-out Hydraulic oil cooling
Cylinder-oil out temp (All cylinders)
Hyd Main pump flow
Pilot line flow
Circulation
P1 line
P2 line
Water Inlet(Hydraulic Oil Cooling)
Water Outlet (Hydraulic Oil Cooling)
Oil inlet flow
Oil outlet flow
Pilot Filter clogging DI
Circulation Filter clogging DI
Lub Filter clogging DI
Hyd Pump motor DE & NDE with Temperature
Hyd Pump Vibration with Temperature
Hyd Oil level (Analog)
Manipulator-L&R Motor Current
Hydraulic Pump Motor (7 Motors)
Profibus Communication error
Ethernet Communication error
Oil contamination level
Forming Profile Offset(Set)
Pilot DC valve feedClientck
P1/P2 valve feedClientck ( 3 setup)
Additional valve feedClientck
Pipe Profile /Ovality(Set)
Forming Pipe Edge Gap(Set)
Siemens SITRANS Ts500
Siemens SITRANS P300
Siemens SITRANS LVL200
Siemens SITRANS F M MAG 5000
KROHNE OPTIFLUX 4300
WIKA PSD-4
SKF CMSS 793V
CR Magnetics/LEM CR5210/HO 150-P
Schneider iEM3255
Parker iCountPD
Micro Epsilon ILD1420-25/ILD1420, 21, 22
Siemens SIMATIC ET 200SP
Honeywell 914CE Series
Keyence LJ-V7000 Series
Cognex In-Sight 7000
X 12
X 1
X 1
X 11
X 1
X 3
X 21
X 11
X 8
X 1
X 4
X 2
X 12
X 2
X 1
Forming Press Equipment @ Client
1 Seimens S7-1500
Machine Parameter types & All parameters that will be captured
My company scope of implementation
Factory Premises
Hyd Main pump pressure
Pilot line pressure
Hydraulic Oil Cooling Water & oil Inlet, outlet Pressure
Bottom Cylinder Inlet Pressure
Top Cylinder Inlet Pressure
Central Lubrication Pressure
Grease Cent Lub system
Pilot Pressure Inlet to Filter
Existing 25 Sensors (from ClientLLUFF, IFM, REXROTH, ABB, VIPA, GE etc)
PLC
MS Azure Cloud
Centralised / Management Reporting
Data processing
Data science
(** Detailed solutioning explained in next 3 slides)

## Slide 3
Surface Inspection
Speed
Flow
visual
Pressure
Temperature
Pressure
Vibration
position
profile
oil contamination
Length
Electrical Panel Room Temp
Water-in Heat Exchanger
Water-out in HE
Hydraulic oil inlet into HE
Hydraulic oil outlet from HE
pilot line pressure
Hot Hydraulic oil inlet Pressure into HE
Coolied hydraulic oil outlet Pressure from He
Main cylinder pressure (top& bottom) Left side
Main cylinder pressure (top& bottom) right side
Die Lifting cylinders (top& bottom) left side
Die Lifting cylinders (top& bottom) right side
Plate holding cylinders(top& bottom) Left side
Plate holding cylinders(top& bottom) Right side
Central lubrication System
Inline Filter pressure difference & Clogging indication
Reciprocating Line Filter Pressure Difference & Clogging indication
Cooling Water Inlet Pressure
Cooling Water outlet Pressure
Die Block
pump
tool position
die position
plate holding cylinders position
Real time length of plate Crimped)
Dent
Rust
Scratch
Surface waviness(camber)
crimping arc profile
Real time length of plate Crimped l
crimping arc profile
Pilot DC valve feedClientck
P1/P2 valve feedClientck ( 3 setup)
Additional valve feedClientck
Forming Pipe Edge Gap(Set)
SMC Digital Flow Switch
Siemens Sitrans P300
OMRON Welding Bead Sensor
Model Name/Number: Sitrans Ts500 from Siemens
Cognex 3D-L4000 or SICK TriSpectorP1000
SICK DX35
Cognex 3D-L4000 or SICK TriSpectorP1000
Parker iCount PD
Siemens Sitrans P DS III
Siemens Sitrans P300
Forming Press Equipment @ Client
1 Seimens S7-1500
Machine Parameter types & All parameters that will be captured for Crimping machine
My Company scope of implementation
MS Azure Cloud
Centralised / Management Reporting
Data processing
Data science
(** Detailed solutioning explained in next 3 slides)

## Slide 4
Temp Sensor
Pressure Sensor
Level Sensor
Vibration Sensor
Contamination Sensor
Proximity Sensor
Siemens S7 1500 PLC
DI Module
AI module
Ladder Logic (calibration of the Analog signals & store the O/P in a TAG)
Edge Desktop
Ethernet / RJ45
MS Azure Cloud
Analog Input (e.g. 0~10 V or 4~20 mAmp)
Digital Input
Remote I/O
Remote I/O
Limit Switch
Etc…etc
~250 ms
(picks up TAG value from the PLC
~MQTT or any standard protocol
SIMATIC S7 Server
SIMATIC S7 Client
OPC UA Server
OPC UA Client
OR
OR
PLC
Factory / Shop Floor
MS Azure Cloud
Real time monitoring Dashboard (SCADA) for supervision
Centralised / Management Reporting
Data processing
Data science
cabbles
(** Detailed solutioning explained in next 3 slides)

## Slide 5: A detailed technical solution architecture of building a Microsoft Azure data platform to propel Data Analytics & AI @ Scale
Data Analysts
Data Scientists
Data Stewards
Data Engineers
Data Ingestion
P
Advanced Analytics and Data Science Zone
Recommended Architecture
Networking and Firewall
Model Packaging
Model Check-In & Containerization
Model Execution
Model Output
End
Consumers
Data Harmonization
(Bronze)
Data Segregation
(Silver)
Model Training
Data Assets
Domain 1
Domain 2
Domain ….n
Domain 1
Domain 2
Domain…n
Domain 1
Domain…n
Domain 2
Data Governance
Data Ingestion Pipeline
IAM Policies
Reusable Assets
Data Operations
Data Privacy and Security
Cloud Datawarehouse (Gold)
Visualization Layer
Data Landing
Raw
Data quality checks metadata
Trusted Data
Insights
Insights
Data Prep Routines
Prepare
Unify
1
2
3
4
5
6
7
8
9
10
11
HOT Path data processing & Visualization
COLD Path data processing & Visualization
Operations Manager
SRE Manager
Plant supervisor
Machine Maintenance Lead
Notes: Done

## Slide 6: Solution Design Notes for Data platform
Architecture Layer | Technical Solution | MS Azure | Google Cloud Platform | AWS
Connectivity between on-premise and cloud | The connectivity established between on-premise to cloud should be secured & have capabilities to Ensure Zero data leakage Ensure In-transit data encryption (if applicable Clientsed on Phase 1 discussions) Ensure Data transmission is happening over a private tunnel only Perform integration testing related to & including Access checks, Sanity testing, Source data load check along with its file size, Data Quality, Data consistency, Data Cleansing, Data Format. | Azure VPN gateway Azure Express Route | API Gateway Cloud VPN Cloud Router | AWS Direct connect AWS transit ateway AWS customer gateway
Data Ingestion | Data ingestion pipelines will have following deliverables/capabilities Frameworks for Real time Event publishing ¦ API & Webhooks¦ Streaming of IoT Data Templatized, metadata driven, build once, use multiple features Verification related to & including - Clienttches are up and running, logs, scheduler job timelines, recon, Meta data, Data completeness, Data consistency, Data Quality, Data integrity, Profiling, Deduplication checks | Azure Data explorer, Azure Data factory for change data capture . Azure Data explorer, Kafka Sink for real time streaming Azure IoT, Azure Event Hubs | Data flow Pub/Sub for event handling Cloud IoT core | AWS Glue for change data capture Amazon managed service for kafka for real time streaming
Data Harmonization | Once the data ingestion pipelines have landed the data (raw data as coming from system of records) into the landing zone, subsequent solution block will have around 10 20+/- pipelines in Bronze zone: Pipelines to convert any source data format(.csv or .json or .xml) into parquet or avro or Iceberg or Hudie format. Capability to prepare parquet files in respective partitioned and indexed zones Verification related to & including to Business transformation, Data Quality, Data Integrity, Record Count, Data Completeness, Logs checks. | Azure data factory as tool Python programming language | Data flow Cloud Data Fusion Python Programming Language | AWS Glue as tool Python programming language
Data Segregation | Once all the parquet files are prepared from the Data harmonization zone, there will be a need to segregate the data into different data domains for Asset management & stock broking, retail trading, proprietary trading, life assurance & retirals, core Clientnking etc. This will not only reduce single point of failure but also enable data scientists to have different individuals focusing on each data domain- which in turn can enable the platform to embrace “Role Clientsed data access control” mechanism. There will be close to 30~ 40 +/- pipelines segregating the data in different data domain buckets/folders and this is silver zone. Data segregation correctness, user role specific, data load validation, Data Correctness, Data Integrity, performance testing , | Azure Data factory Python programming language Azure FaaS (for implementing event driven architecture) | Data flow Python Programing Language Big Query | AWS Glue as tool Python programming language AWS Lambda (for implementing even driven architecture)
Model training | Once the data has is placed in segregated folders (per data domain) in silver zone, data scientists can start explorative data analysis on training their individual models with the data set available. <<SI>> team will do the technical capability building by setting up Azure ML Studios, and Databricks services Train sample Models (1 or 2) as a pilot & establish the capability including hand over of relevant documentation to BOV data scientists | Azure ML Studio workspace Juypter notebooks Databricks | Cloud ML engine Tensor Flow enterprise VertexAI Jupyter Notebook | AWS Sagemaker Jupyter notebooks Databricks AWS EMR
1
2
3
4
5
Solution capabilities
Notes: Done

## Slide 7
Architecture Layer | Technical Solution | MS Azure | GCP | AWS
Model packaging | After Client data scientists have trained their individual respective models and are satisfied with the model scores being generated, the models need to be packaged into docker containers using git. <<SI>> team will set up the repositories (for check in), user ids and relevant pipelines. | git Docker Azure Kubernetes Azure devops | git Docker GKe Kubernetes Engine | git docker
Model check in | After the docker images (for models) are ready to be run as executables, they need to be checked in into a registry so that they can be accessed by a “pull” pipeline or via an API. <<SI>> team will perform this for 1 or 2 sample models, expose the APIs and ensure that the process is streamlined for rest of the models & usage documentation available to BOV team | Azure container registry Azure Container instance for execution |  | AWS Elastic container registry AWS Fargate for execution platform
Model execution pipeline | For trained/ tested/ checked-in models, <<SI>> team will configure ETL pipelines so that they can run on a scheduled or an event driven architectural pattern or an ad-hoc need Clientsis to generate the output needed by CRM team to consume as output. | Azure Databricks in Data Analytics mode pySpark programming language | Data Bricks Pyspark | Databricks in Data Analytics mode pySpark programming language
Model output | This is the published zone where the output of the models will be placed for CRM systems to consumes. This zone will be built per data domain and scores/output from models will be placed in the form of files, so that CRM can consume the outputs. Integration protocols (file Clientsed or DB Clientsed, or API Clientsed etc.) between Analytics Data Lake and CRM application will be finalized during Phase 1 discussion- <<SI>> team is going to define the patterns and set up the integrations only. | Azure Data lake storage | Google Cloud Storage | AWS S3
Data Lake Operations | Audit logs will be captured in a centralized place. <<SI>> to define the “location” & assist log capturing strategy as below. Discuss relevant Alerts, thresholds, monitoring metrices and alarms that needs to be configured during Phase 1 Assist in real implementation of solutioning which Clientsically will constitute of setting up above rules and respective point of contacts. BOV should set up an early warning system to enable predictive, prescriptive and proactive incident management system | Azure Monitoring service Azure notification Elastic Search (optional) Unravel (optional) | Cloud IAM Cloud Monitoring Cloud Deployment Manage Elastic Search (optional) Unravel (optional) | AWS cloudwtach AWS SNS, SQS, SES AWS ELK(optional) Unravel(optional)
Data privacy and security | Define Data privacy and security process for DSAR Define Security requirements Tool evaluation on how to implement security policies is out of scope but can be taken in scope Clientsed on phase 1 requirements | Azure active directory | Cloud KMS and EKM | AWS Native services
6
7
9
10
8
11
Solution Design Notes for Data platform
Notes: Done