## Slide 1
MEE224 THERMAL ENGINEERING
Second Law of thermodynamics
Reference books:
“Thermodynamics: An Engineering approach” by Cengel
“Engineering Thermodynamics” by R.K. Rajput
“Engineering Thermodynamics” by P. K. Nag

## Slide 2
Whether this process can be reversed?
Introduction to Second law of thermodynamics
According to first law of thermodynamics, Energy lost by the tea should be equal to the energy gained by the surrounding (Law of energy conservation)
Qlost, coffee = Qgained, surrounding
I mean, can energy transfer happen again, from surrounding to heat the cold coffee?
This process is natural and spontaneous
Electricity is passed through the copper coil
If we reverse the process!
Heat is produced
Can we produce electricity?
Heat is added
Example 2
Example 1
Naturally Not possible
First law only states the energy transformation from one form to another…
But it does not state, in which direction the energy can flow…
Limitation of First law!
That is why, Second law of thermodynamics was framed!
In general, this law states that,
Energy can flow only in certain direction, but not in the reverse direction…
Even though, this is not violating the first law of thermodynamics, this process cannot happen.
Naturally it is not possible

## Slide 3
Introduction to Second law of thermodynamics
Kelvin Planck statement
It is impossible to construct a heat engine that operates in a cyclic process, that absorbs heat from a single reservoir and convert all of that heat into work.
Second law of thermodynamics, helps us to understand the energy transfer in terms of quantity and quality
Heat source
Heat engine
Work output
100%
100%
Impossible!
Consider a Car…
100% of fuel is not utilized to run the car. There is always a heat rejection and heat loss.
Heat engine
Heat sink
Heat rejection
Useful work
Heat source
No heat engine is 100% efficient
Some energy must be always rejected to the cooler reservoir.

## Slide 4
Energy balance and efficiency of a heat engine (Kelvin Planck statement)
Qin : Amount of heat supplied to steam in boiler from a high-temperature source at constant pressure
Qout : Amount of heat rejected from steam in condenser to a low-temperature sink at constant pressure
Wout : Amount of work delivered by steam as it expands in turbine
Win : Amount of work required to compress water to boiler pressure
Energy balance in steam power plant
1
How to find the net-work (), that we get out of the system?
(kJ)
2
From equations 1 and 2, we can write as,
(kJ)
3
Generally, how performance is evaluated?
In terms of thermal systems, we use the word “Efficiency”
Thermal efficiency of a heat engine is always less than 1 or less than100%, as both Qout and Qin are always positive values and Qout< Qin
HP and HT
Superheated steam
LP and HT
Mixture steam
LP and LT
liquid
LP and LT
liquid

## Slide 5
Introduction to Second law of thermodynamics
Kelvin Planck statement
Clausius statement
It is impossible to construct a heat engine that operates in a cyclic process, that absorbs heat from a single reservoir and convert all of that heat into work.
It is impossible to develop a device (system) to occur which is operating in a cycle, where, the heat transfer occurs from a cooler body to a hotter body, without any help from an external work.
Second law of thermodynamics, helps us to understand the energy transfer in terms of quantity and quality
Heat source
Heat engine
Work output
100%
100%
Impossible!
Consider a Car…
100% of fuel is not utilized to run the car. There is always a heat rejection and heat loss.
Heat engine
Heat sink
Heat rejection
Useful work
Hot body
System
Cold body
Work
input
We have to give some work to transfer heat from cold to hot body. Cannot happen naturally
Consider a Refrigerator…
We are supplying energy (work), to reduce the refrigerator’s temperature below atmospheric temperature.
Generally cooling occurs naturally, but refrigeration needs some external work
Heat source
No heat engine is 100% efficient
Some energy must be always rejected to the cooler reservoir.

## Slide 6
Just think!!!!
Imagine that you kept a refrigerator inside the insulated room.
You kept it open and switched it on
What will be the temperature of the insulated room after one hour?
Time | Temperature rise from 27 oC in 3m2 room
1 min | 1.32 oC
5 min | 6.6 oC
10 min | 13.2 oC
30 min | 39.6 oC
1 hour | 79.2 oC
Do you think that the room will be cooled?
Answer is, the temperature of the insulated room will be 79.2 oC higher than the initial room temperature
Because….!
The refrigerant flows continuously in the refrigerator to absorb heat from the room
This heat should be lost to the surrounding with the help of condenser which is located at back side of refrigerator.
But, here the heat is again dissipated in to the room, as the condenser is also inside the room. So this process happens continuously which will not reduce the temperature of the room.
In addition, continuous running of compressor, condenser fan due to electric supply, naturally generates heat which is also dissipated inside the room.
So, keeping the refrigerator open inside a room, will always increase the temperature of the room.
Note: Only if the room is 100% insulated
By the way, this will not happen in real time, as the walls and ventilations will dissipate the heat continuously outside. And compressor will shutdown due to over heat.
There should be an external energy or work given to the system, to transfer heat from cold body to hot body.
Proving Clausius statement

## Slide 7
Coefficient of Performance (COP) of a refrigerator
QL : Amount of heat absorbed from the space where cooling is needed
QH : Amount of heat rejected to the atmosphere
Wnet, in : Amount of work supplied as input, to get the desired cooling effect
1
What is the desired output here?
(kJ)
What is the required input here?
Coefficient of Performance (COP) of a refrigerator should be greater than 1.
In refrigerator, we do not use the word “efficiency”. But we use “Coefficient of Performance”
Amount of work required to run the compressor.
Amount of heat from refrigerated space to be removed
(Cooling effect)
2
Where, >
HP and HT
vapor
LP and LT
vapor
LP and LT
Liquid
HP and LT
liquid
Commercial refrigerators have Coefficient of Performance (COP) ranging between 2 and 3
Inside refrigerator
Backside of refrigerator

## Slide 8
Heat pumps
QL : Amount of heat absorbed from the outside environment
QH : Amount of heat supplied in to the living room
Wnet, in : Amount of work supplied as input, to get the desired heating effect
What is the desired output here?
(kJ)
What is the required input here?
COP of a pump = COP of a refrigerator +1.
Heat pumps are devices, that transfer the thermal energy from cold space to the warm place
Amount of work required to run the device.
Amount of heat supplied in to the room (Heating effect)
2
Consider that, you are in Sweden, at winter season. The temperature outside is 0 oC. So, you need a device that supplies heat in to the room to maintain the room’s temperature at 25 oC.
T = 0 oC
T = 25 oC
Work input
Heat pump
1
1
We know that,

## Slide 9
Difference between Refrigerator, Air conditioner and Heat pump
Refrigerator
Air conditioner
Heat pump
Refrigerator is a device, used to absorb heat from the inner space, and dissipate that heat to the surrounding.
This makes the food and vegetables cooler.
Common everywhere in the world
Air conditioner is a device, used to absorb heat from the living room, and dissipate that heat to the surrounding.
This makes the living room cooler.
Common in Hot countries.!
Heat pump is a device, used to absorb heat from outer space, and dissipate that heat in to the living room.
This makes the living room warmer.
Common in Cold countries.!
Rejects heat to the surrounding
Absorbs heat from inner space
Rejects heat to the surrounding using condenser
Absorbs the heat from living room
Rejects heat in to the Living room
Absorbs heat from the surrounding

## Slide 10
Reversible and Irreversible processes
Reversible process
Reversible process
So, if the system follows the same path to return its original state and if there is no change in the system and its surrounding, it is called reversible process.
Irreversible process
So, if the system cannot return to its initial position, it is called reversible process.
Initial state
P
V
Final state
Initial state
P
V
Final state
Not possible in real time
All the real time devices are irreversible
Then why should we study about reversible process, if it is not practically possible?
Irreversibility occur due to the following reasons:
2. Unrestrained expansion
1. Friction
Vacuum
Gas expanded
3. Heat transfer
5. Inelastic deformation of solids
6. Chemical reactions
4. Mixing of two fluids
The reason is that, the reversible process shows the maximum theoretical efficiency of device, by absorbing least amount of work during compression.
Infinitesimally slow compression
Real time (fast) compression
Almost no heat loss
Almost no friction loss
Friction is present and so, heat is also produced.
Because of friction, you need to give more work (energy) to move the piston.
There are almost no losses. So you apply very very less work (energy) to move the piston
Friction and heat
Quasi static process

## Slide 11
Carnot Engine
The best known reversible cycle is the “Carnot Cycle”.
An imaginary heat engine with complete reversible processes
Introduced by “Sadi Carnot” in 1824
Process 1-2: Isothermal Expansion
Process 2-3:Isentropic (Adiabatic) Expansion
Process 4-1:Isentropic (Adiabatic) Compression
Process 3-4: Isothermal Compression
P
V
1
2
3
4
QH
QL
TH
TL

## Slide 12
Carnot Engine
The best known reversible cycle is the “Carnot Cycle”.
An imaginary heat engine with complete reversible processes
Introduced by “Sadi Carnot” in 1824
1
2
3
3
4
4
Heat is added to maintain the Internal energy of gas, during expansion (maintaining constant temperature).
No heat transfer in or out, and further expanded only using the internal energy of the gas (temperature of gas reduces)
2
Gas is compressed along with heat rejection, to maintain to maintain the Internal energy of gas (maintaining constant temperature).
Gas is further compressed with any heat transfer in or out, to increase the Internal energy (increase the temperature as in initial state)
1
Process 1-2: Isothermal Expansion
Process 2-3:Adiabatic Expansion
Process 4-1:Adiabatic Compression
Process 3-4: Isothermal Compression
Qsupplied
Qrejected
No change in Internal energy
No change in Internal energy
Internal energy
reduces
Internal energy
increases
No change in temperature
Temperature reduces
Temperature increases
No change in temperature
U = C
T = C
U =
T =
U =
T =
U = C
T = C

## Slide 13
Process 1-2: Isothermal Expansion
Process 2-3:Isentropic (Adiabatic) Expansion
Process 4-1:Isentropic (Adiabatic) Compression
Process 3-4: Isothermal Compression
P
V
1
2
3
4
P
V
1
2
3
4
Carnot Cycle
Reversed Carnot cycle
QH
QL
QL
QH
Process 1-2: Isentropic (Adiabatic) compression
Process 2-3:Isothermal heat rejection
Process 3-4: Isentropic (Adiabatic) expansion
Process 4-1: Isothermal heat absorption
Carnot heat engine
Carnot refrigeration
TH
TL