## Slide 1: Comptia Network Plus
Lesson 1 introduction

## Slide 2: LESSON INTRODUCTION
Computer networks are complex systems that incorporate multiple functions, standards, and proprietary technologies. The Open Systems Interconnection (OSI) model is used to try to simplify some of this complexity. It divides network technologies between seven functional layers. This makes it easier to separate and focus on individual concepts and technologies while retaining an understanding of relationships to the functions of technologies placed in other layers.

## Slide 3: LESSON INTRODUCTION
This lesson uses the OSI model to give you an overview of the technologies that
you will be studying in the rest of the course. You will compare the functions of
these layers in the OSI model and apply those concepts to the installation and
configuration of a small office/home office network.

## Slide 4: Open Systems Interconnection (OSI) model
The Open Systems Interconnection (OSI) model breaks the data communication process into discrete layers. Being able to identify the OSI layers and compare the functions of devices and protocols working at each layer will help you to plan, implement and troubleshoot networks.
A network is two or more computer systems that are linked by a transmission medium and share one or more protocols that enable them to exchange data. You
can think of any network in terms of nodes and links. The nodes are devices that send, receive, and forward data and the links are the communications pathways
between them.

## Slide 5: Open Systems Interconnection (OSI) model
The International Organization for Standardization (ISO) developed the Open Systems
Interconnection (OSI) reference model to promote
understanding of how components in a network system work.

## Slide 6: Open Systems Interconnection (OSI) model

## Slide 7: Data Encapsulation and Decapsulation
A network protocol is a set of rules for exchanging data in a structured format.
A network protocol has two principal functions:
Addressing—Describing where data messages should go. At each layer, there are different mechanisms for identifying nodes and rules for how they can send and receive messages.
• Encapsulation—Describing how data messages should be packaged for transmission. Encapsulation is like an envelope for a letter, with the distinction that each layer requires its own envelope. At each layer, the protocol adds fields in a header to whatever data (payload) it receives from an application or other protocol.

## Slide 8: Data Encapsulation and Decapsulation
A network will involve the use of many different protocols operating at different layers of the OSI model. At each layer, for two nodes to communicate they must be
running the same protocol. The protocol running at each layer communicates with its equivalent (or peer) layer on the other node. This communication between nodes
at the same layer is described as a same layer interaction. To transmit or receive a communication, on each node, each layer provides services for the layer above and
uses the services of the layer below. This is referred to as adjacent layer interaction.

## Slide 9: Data Encapsulation and Decapsulation

## Slide 10: Data Encapsulation and Decapsulation
When a message is sent from one node to another, it travels down the stack of
layers on the sending node, reaches the receiving node using the transmission
media, and then passes up the stack on that node.
At each level (except the physical layer), the sending node adds a header to the data payload, forming a “chunk” of data called a protocol data unit (PDU). This is the process of encapsulation.
For example, on the sending node, data is generated by an application, such as the
HyperText Transfer Protocol (HTTP), which will include its own application header.
At the transport layer, a Transport Control Protocol (TCP) header is added to this
application data. At the network layer, the TCP segment is wrapped in an Internet
Protocol (IP) header. The IP packet is encapsulated in an Ethernet frame at the
data link layer, then the stream of bits making up the frame is transmitted over the
network at the physical layer as a modulated electrical signal.

## Slide 11: Data Encapsulation and Decapsulation
The receiving node performs the reverse process, referred to as decapsulation. It receives the stream of bits arriving at the physical layer and decodes an Ethernet
frame. It extracts the IP packet from this frame and resolves the information in the IP header, then does the same for the TCP and application headers, eventually
extracting the HTTP application data for processing by a software program, such as a web browser or web server.

## Slide 12: Layer 1—Physical
The physical layer (PHY) of the OSI model (layer 1) is responsible for the transmission
and receipt of the signals that represent bits of data from one node to another node.
Different types of transmission media can be classified as cabled or wireless:
• Cabled—A physical signal conductor is provided between two nodes. Examples
include cable types such as copper or fiber optic cable. Cabled media can also be
described as bounded media.
• Wireless—Uses free space between nodes, such as microwave radio. Wireless
media can also be described as unbounded media.

## Slide 13: Layer 2—Data Link
The data link layer (layer 2) is responsible for transferring data between nodes on
the same logical segment. At the Data Link layer, a segment is one where all nodes can send traffic to one another using hardware addresses, regardless of whether
they share access to the same media. A layer 2 segment might include multiple physical segments. This is referred to as a logical topology. Relatively few networks are based on directly connecting hosts together. Rather than making hosts establish direct links with one another, each host is connected to a central node, such as a switch or a wireless access point. The central node provides a forwarding function, receiving the communication from one node and sending it to another. The addresses of interfaces within the same layer 2 segment are described as local addresses or hardware addresses.

## Slide 14: Layer 2—Data Link
Devices that operate at the data link layer include:
• Network adapter or network interface card (NICs)—An NIC joins an end system host to network media (cabling or wireless) and enables it to communicate over the network by assembling and disassembling frames.
• Bridge—A bridge is a type of intermediate system that joins physical network segments while minimizing the performance reduction of having more nodes
on the same network. A bridge has multiple ports, each of which functions as a network interface.
• Switch—An advanced type of bridge with many ports. A switch creates links between large numbers of nodes more efficiently.
• Wireless access point (AP)—An AP allows nodes with wireless network cards to communicate and creates a bridge between wireless networks and wired ones.

## Slide 15: Layer 3—Network
The network layer (layer 3) is responsible for moving data around a network of networks, known as an internetwork or the Internet. While the data link layer is
capable of forwarding data by using hardware addresses within a single segment, the network layer moves information around an internetwork by using logical
network and host IDs. The networks are often heterogeneous; that is, they use a variety of physical layer media and data link protocols. The main appliance working at layer 3 is the router.

## Slide 16: Layer 3—Network

## Slide 17: Layer 3—Network
The network layer forwards information between networks by examining the destination network-layer address or logical network address. The packet is forwarded, router by router (or hop by hop), through the internetwork to the target network. Once it has reached the destination network, the hardware address can be used to deliver the packet to the target node.

## Slide 18: Layer 4—Transport
The first three layers of the OSI model are primarily concerned with moving frames
and datagrams between nodes and networks. At the transport layer—also known
as the end-to-end or host-to-host layer—the content of the packets becomes
significant. Any given host on a network will be communicating with many other
hosts using many different types of networking data. One of the functions of the
transport layer is to identify each type of network application by assigning it a
port number. For example, data requested from an HTTP web application can be
identified as port 80, while data sent to an email server can be identified as port 25.

## Slide 19: Layer 4—Transport
At the transport layer, on the sending host, data from the upper layers is packaged as a series of layer 4 PDUs, referred to as segments. Each segment is tagged with
the application’s port number. The segment is then passed to the network layer for delivery. Many different hosts could be transmitting multiple HTTP and email packets at the same time. These are multiplexed using the port numbers along with the source and destination network addresses onto the same link.
At the network and data link layers, the port number is ignored—it becomes part of the data payload and is invisible to the routers and switches that implement the addressing
and forwarding functions of these layers. At the receiving host, each segment is decapsulated, identified by its port number, and passed to the relevant handler at the application layer.

## Slide 20: Layer 4—Transport
Devices working at the transport layer include multilayer switches—usually working as load balancers—and many types of security appliances, such as more advanced
firewalls and intrusion detection systems (IDSs).

## Slide 21: Layer 5—Session
Most application protocols require the exchange of multiple messages between the client and server. This exchange of such a sequence of messages is called a
session or dialog. The session layer (layer 5) represents functions that administer the process of establishing a dialog, managing data transfer, and then ending (or
tearing down) the session.

## Slide 22: Layer 6—Presentation
Layer 6—Presentation
The presentation layer (layer 6) transforms data between the format required for the network and the format required for the application. For example, the
presentation layer is used for character set conversion, such as between American Standard Code for Information Interchange (ASCII) and Unicode. The presentation
layer can also be conceived as supporting data compression and encryption.

## Slide 23: Layer 7—Application
The application layer (layer 7) is at the top of the OSI stack. An application layer protocol doesn’t encapsulate any other protocols or provide services to any
protocol. Application-layer protocols provide an interface for software programs on network hosts that have established a communications channel through the
lower-level protocols to exchange data.
More widely, upper-layer protocols provide most of the services that make a network useful, rather than just functional, including web browsing, email and
communications, directory lookup, remote printing, and database services.

## Slide 24: OSI Model Summary
The following image summarizes the OSI model, listing the PDUs at each layer, along with the types of devices that work at each layer.